## Slide 1
AVR Assembly
Slight modification of slides shared by Dr. Rehan Ahmed
Instructor: Asra Abid Siddiqui [asiddiqui.phd20seecs@seecs.edu.pk]
CS-336: Embedded Systems

## Slide 2: Modeling Finite State Machines
Some More Assembly Instructions …

## Slide 3: Subtraction
SUB Rd, Rs
  Rd = Rd – Rs
Example:
  SUB R25, R9
    R25 = R25 - R9
  SUB R17, R30
    R17 = R17 - R30
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 4: Increment and Decrement
INC Rd
  Rd = Rd + 1
Example:
  INC R25
    R25 = R25 + 1
DEC Rd
  Rd = Rd - 1
Example:
  DEC R23
    R23 = R23 - 1
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 5: Modeling Finite State Machines
AVR Memory Space
Two Kinds of Memory Spaces:
Code Memory
Data Memory

## Slide 6: AVR Data Memory

## Slide 7: AVR Data Memory: Data Memory Space
Data memory composed of:
GPRs
I/O Memory
Internal data SRAM

## Slide 8: Data Address Space
Data memory composed of:
GPRs
I/O Memory
Internal data SRAM

## Slide 9: AVR Data Memory Space: GPRs
GPRs:
  Take 32 bytes of data memory
  Address location $00 - $1F (always)

## Slide 10: AVR Data Memory Space: I/O Memory
I/O Memory (SFR):
    Dedicated to specific functions such as:
      Status register
      Timers
      Serial communication etc.
    I/O Memory locations depend on the number of pins and peripheral functions supported by a device
      At least all the families have 64 bytes
I/O Registers

## Slide 11: AVR Data Memory Space: I/O Memory

## Slide 12: AVR Data Memory Space: Internal SRAM
Internal SRAM:
  aka Scratch Pad memory
    Used for storing data and parameters

## Slide 13: Data Address Space
LDS Rd, addr ;Rd = [addr]
Example:
LDS R1, 0x60
LDS (Load direct from data space)
STS addr,Rd ;[addr]=Rd
Example:
STS 0x60,R15 ; [0x60] = R15
STS (Store direct to data space)
Example: Write a program that stores 55 into location 0x80 of RAM.
Solution:
LDI R20, 55 ;R20 = 55
STS 0x80, R20 ;[0x80] = R20 = 55
Example: Write a program that copies the contents of location 0x80 of RAM into location 0x81.
Solution:
LDS R20, 0x80 ;R20 = [0x80]
STS 0x81, R20 ;[0x81] = R20 = [0x80]
Example: Add contents of location 0x90 to contents of location 0x95 and store the result in location 0x313.
Solution:
LDS R20, 0x90 ;R20 = [0x90]
LDS R21, 0x95 ;R21 = [0x95]
ADD R20, R21 ;R20 = R20 + R21
STS 0x313, R20 ;[0x313] = R20
Example: What does the following instruction do?
LDS R20,2
Answer:
It copies the contents of R2 into R20; as 2 is the address of R2.
Solution:
LDI R20, 0x53 ;R20 = 0x53
STS 0x5E, R20 ;SPH = R20
Example: Store 0x53 into the SPH register. The address of SPH is 0x5E

## Slide 14
Solution:
LDS R20, 0x53 ;R20 = 0x53
STS 0x5E, R20 ;SPH = R20

## Slide 15: Data Address Space
IN Rd,IOaddress ;Rd = [addr]
Example:
IN R1, 0x3F ;R1 = SREG
IN R17,0x3E ;R17 = SPH
IN (IN from IO location)
OUT IOAddr,Rd ;[addr]=Rd
Example:
OUT 0x3F,R12 ;SREG = R12
OUT 0x3E,R15 ;SPH = R15
OUT (OUT to I/O location)
Example:
OUT SPH,R12 ;OUT 0x3E,R12
IN R15,SREG ;IN R15,0x3F
Using Names of I/O registers
Example: Write a program that adds the contents of the PINC I/O register to the contents of PIND and stores the result in location 0x90 of the SRAM
Solution:
IN R20,PINC ;R20 = PINC
IN R21,PIND ;R21 = PIND
ADD R20,R21 ;R20 = R20 + R21
STS 0x90,R20 ;[0x90] = R20

## Slide 16: Reading Assignment
The AVR Microcontroller and Embedded Systems: Using Assembly and C by Mazidi et al., Prentice Hall
  Chapter 2: 2.1-2.3

## Slide 17
THANK YOU